DESCRIPTION

Electric cables for industrial use, symmetric stranded, two shields and LSHF outer sheath. Suitable for connexion of frequency converters.

Construction according to IEC-60502.

CONSTRUCTION

1 - Conductor:				Flexible bare copper, class 5				a/EN 60228

2 - Insulation:				Cross linked polyethylene, type XLPE			a/IEC 60502-1

Identification: brown, black, grey, 3 green/yellow

Assembly of cores: symmetric stranded

3 – 1st shield:				Aluminium/polyester tape

Coverage: 100%

4 – 2nd shield:				Tinned copper wire braid.

Coverage > 65%

5 – Outer sheath			Halogen free compound, type ST8, black colour		a/IEC 60502-1

TECHNICAL SPECIFICATIONS

Rated voltage:				0.6 / 1 kV

Test voltage:				3.500 V

Operating temperature:			-15 to +90 ºC

Maximum short-circuit temperature:	250 ºC (max. 5 s)

Flame retardant:			Complies						a/IEC 60332-1

Fire retardant:				Complies						a/IEC 60332-3

Low Smoke emission:			Complies, transmittance > 60%				a/IEC 61034-2

Halogen free:				Complies, pH≥4.3; conductivity ≤10 µS/mm		a/IEC 60754-2

DATA AND DIMENSIONS

Dimensions and weights are approximates, subject to small variations due to process.

| Cross Section mm² | Resistance Ω/km a 20ºC | Insulation thickness, mm | Outer sheath thickness, mm | Outer Ø mm | Weight Kg/km |
| --- | --- | --- | --- | --- | --- |
| 3x6+3G1 | 3.30 / 19.5 | 0.7 / 0.7 | 1.4 | 16.1 | 344 |
| 3x10+3G1.5 | 1.91 / 13.3 | 0.7 / 0.7 | 1.4 | 17.0 | 491 |
| 3x16+3G2.5 | 1.21 / 7.98 | 0.7 / 0.7 | 1.5 | 185 | 674 |
| 3x25+3G4 | 0.780 / 4.95 | 0.9 / 0.7 | 1.6 | 22.5 | 999 |
| 3x35+3G6 | 0.554 / 3.30 | 0.9 / 0.7 | 1.8 | 24.7 | 1326 |
| 3x50+3G10 | 0.386 / 1.91 | 1.0 / 0.7 | 1.9 | 30.3 | 1932 |
| 3x70+3G10 | 0.272 / 1.91 | 1.1 / 0.7 | 2.0 | 35.2 | 2642 |
| 3x95+3G16 | 0.206 / 1.21 | 1.1 / 0.7 | 2.1 | 39.5 | 3313 |
| 3x120+3G25 | 0.161 / 0.780 | 1.2 / 0.9 | 2.2 | 43.7 | 4328 |
| 3x150+3G25 | 0.129 / 0.780 | 1.4 / 0.9 | 2.4 | 48.2 | 5222 |
| 3x185+3G35 | 0.106 / 0.554 | 1.6 / 0.9 | 2.5 | 52.8 | 6567 |
| 3x240+3G50 | 0.0801 / 0.386 | 1.7 / 1.0 | 2.8 | 61.0 | 8656 |

# Text boxes

5

4

3

2

1